## Slide 1: SONiC Configuration Management
Alberto Gonzalez Prieto, Microsoft

## Slide 2: Requirements
Schema formalization
  Easy to understand by developers and clients
Model validation
  Tools for model validation
Management agents (e.g., rest, restconf, cli)
  Adding/modifying yang models requires no additional work on the config management agents
  I.e., (mostly) automated generation of management agents
Single entry point for config
  Centralized entity all configuration operations go through
  Adding/modifying yang models requires no additional work on this entity
  Management-agent-agnostic
Run-time
  Data instance validation
  Automated configuration of the backend (i.e., redis, SONiC apps, etc)
Support for operations (i.e., yang rpc’s. E.g., reset counters)

## Slide 3: Opportunities & Challenges
Opportunities
  Not a new problem
  Yang is very mature: ~10 years & inherits SMI’s learnings
  Several well tested open-source tools for
    Model validation
    Instance validation
    Configuration operations
Challenges
  Standard vs SONiC-based models
    Model transformation can be arbitrarily complex
  Config validation against whole running config
    Duplicating the running config in the validator is the trivial, yet expensive (space) mechanism

## Slide 4: Automating Configuration Operations to backend (e.g. Redis)

## Slide 5: Automating Configuration Operations to Redis
Approach
  Leverage Yang annotations
    Map yang objects to redis table configuration
  Include in the Yang definition how Yang nodes map to Redis DB configuration (or any other backend)
    Following Config_db.json
    The json is parameterized w/ relative yang paths (<path>)
Advantages
  Leverages existing yang tools
  Adding / modifying Yangs requires no additional coding

## Slide 6: Example for Vlan
container interface {
list vlan {
soniccfg:redis-cfg "{
'VLAN' : { // Table name
'<./vlan-id>' : { // Table key (parameterized)
'vlanid' : '<./vlan-id>‘ // Key-value pairs (parameterized)
'cidr' : 'CIDR:<./ip-prefix>' // made up for illustration
}
}
} ";
key "vlan-id";
leaf vlan-id { type vlan-id; }
leaf ip-prefix { type inet:ip-prefix;}
(…)

## Slide 7: Validating Yang Config Data
A non-trivial case
Vlan members cannot be part of a lag that is a Vlan lag member

## Slide 8: “Must” statemement + xpath
The Yang must statement is used for specifying valid data
It takes an xpath that must evaluate to true for the data to be valid
Pros
  Requires no code writing by leveraging existing Yang tools
  Xpath has high expressive power
Cons
  Complex constraints are not always trivial to write
Next, we show how to express a non-trivial case:
  Vlan members cannot be part of a lag that is a lag member of that Vlan

## Slide 9: The interfaces and the lags
container ifaces {
list iface {
key "iface-id";
leaf iface-id { type string;}
} } // end of container ifaces
container lags {
list lag {
key "lag-id";
leaf lag-id { type string; }
container members {
list member {
key "member-id";
leaf member-id {
type leafref {
path "../../../../../ifaces/iface/iface-id";
}
} } } } } // end of container lags
+--rw ifaces
| +--rw iface* [iface-id]
| +--rw iface-id string
+--rw lags
+--rw lag* [lag-id]
+--rw lag-id string
+--rw members
+--rw member* [member-id]
+--rw member-id -> ../../../../../ifaces/iface/iface-id

## Slide 10: The vlans, members and lag-members
container vlans {
list vlan {
key "vlan-id";
leaf vlan-id { type vlan-id;}
container members {
list member {
key "iface";
leaf iface {
type leafref { path "../../../../../ifaces/iface/iface-id";}
must "count(current()/../../../../../lags/lag[lag-id = (current()/../../../lag-members/lag-member/lag-id/text())]/members/member[member-id = current()]) = 0" {
error-message "A vlan interface member cannot be part of a vlan lag member";
} } } } // End of container members
container lag-members {
list lag-member {
key "lag-id";
leaf lag-id {
type leafref { path "../../../../../lags/lag/lag-id"; }
} } } // End of container lag-members
} } // End of container vlans
+--rw vlans
| +--rw vlan* [vlan-id]
| +--rw vlan-id vlan-id
| +--rw members
| | +--rw member* [iface]
| | +--rw iface -> ../../../../../ifaces/iface/iface-id
| +--rw lag-members
| +--rw lag-member* [lag-id]
| +--rw lag-id -> ../../../../../lags/lag/lag-id
+--rw ifaces
| +--rw iface* [iface-id]
| +--rw iface-id string
+--rw lags
+--rw lag* [lag-id]
+--rw lag-id string
+--rw members
+--rw member* [member-id]
+--rw member-id -> ../../../../../ifaces/iface/iface-id