## Slide 1
SONiC Management Framework –Proposal

## Slide 2: Framework High-level Requirements
Provide an Infrastructure for UI development for SONiC, including some client UIs
Support smooth integration of a variety of Standards-based and proprietary data models
  Standard YANG models (e.g. OpenConfig, IETF, IEEE)
  Industry-standard CLI feel (details TBD)
Support easy integration of OpenAPI server-side implementations
Multiple protocols/Interfaces, including concurrency between them: -
  CLI
  gNMI
  REST/RESTCONF
  SNMP
  NETCONF
Unified security using standard network services (e.g. RADIUS, TACACS+, LDAP)
  Authentication - including certificate-based
  Authorization - Role-based
Ease of use for developer workflow
  Specify data model and auto-generate as much as possible from there
Fit with existing SONiC Architecture and Management
  Co-exist with what exists today - backward compatibility
  Don’t place additional requirements upon existing features and infrastructure
Support Validation and Error Handling - data model, platform capability/scale, dynamic resources
Packageable – SONiC users can pick and choose only the pieces they need

## Slide 3: Design

## Slide 4: Config Validation Library
Use cases :
Startup config (config_db.json) validation
Key and Payload validation for CRUD operations inside TransLib
Key and field(s) validation from other application like Click based Python CLI
ABNF Schema
YANG Schema with metadata
Pyang Compiler
Config Validation Library
Redis DB
Common code
Feature specific custom code
Third party
Generated code
Syntax Check
Semantic Check
Platform check
YANG Schema with metadata
Custom Validation
Build Time
Run Time
Platform Specific Data
ABNF JSON
Translator
(to YANG XML)
Manually written

## Slide 5: CLI Design

## Slide 6: gNMI Server Integration

## Slide 7
Backup

## Slide 8: App Registration

## Slide 9: REST SET Operation

## Slide 10: REST GET Operation

## Slide 11: Approach
TransLib - Library for Management application servers
REST server, gNMI server and TransLib all in GO
Marshalling and unmarshalling using YGOT
Concurrent writes from different management applications without lock
Integration into KLISH based CLI framework
Config validation

## Slide 12: Design contd ...
Pyang Compiler
  An extensible YANG validator and OpenAPI Spec generator.
YGOT Generator
  Collection of Go utilities for generating Go Structures, validating contents in the Go structures, rendering Go Structure to output format such as JSON.
Swagger Tool
  Generates Client SDK, Server Stub and API documentation based on OpenAPI Spec.
Client SDK
  Swagger generated APIs used to communicate with REST server from a REST client/CLI.
REST Gateway (Server)
  GO based REST server generated using swagger.
  REST Request Handler
    All REST requests from Northbound land here
    Invokes common handler for CRUD operations with path and Payload
    Calls appropriate Translib functions based on CRUD operation.
GNMI Server
    Existing GNMI server in SONiC extended for YANG based support
    GNMI Request Handler
      Handles Set/Get/Subscribe/Capability request.
      Calls appropriate Translib functions based on requested operation

## Slide 13: Design contd ...
TransLib (GO)
GO based Translation library to convert data in YANG to Redis(ABNF) format and vice versa, validate config data and write to Redis/Non-DB database.
  Translib Infra
    GO bind-Objects
      GO bindings generated using YGOT. Converts the incoming payload to YGOT structures, which is given to App modules
    Request Handler
      All requests from management servers land here.
    App Interface
      App modules registers with it dpathng TransLib initialization
      Invokes appropriate app module specific implementation
  App Modules
    YGOT structure to ABNF key value pairs - write, ABNF key value pairs to YGOT structure - read
    Translates, validates and converts data.
    Facilitates breaking bulk operation into multiple operations suitable for Redis transaction
  DB Access
    Provides access to Redis DB using Go-Redis package
    Supports transaction
  Config Validation
    Validates a JSON buffer against given ABNF schema. Carries-out semantic, syntactic, parameter, type and range validation as well as platform and inter-dependency validation. Uses code generated from a schema definition

## Slide 14: Config Validation Library
module: sonic-vlan
+--rw VLAN* [name]
| +--rw name string
| +--rw vlanid? uint16
| +--rw members* -> /sif:PORT_TABLE/ifname
+--rw VLAN_MEMBER* [name ifname]
+--rw name -> ../../VLAN/name
+--rw ifname -> /sif:PORT_TABLE/ifname
+--rw tagging_mode? scommon:tagging_mode
ABNF JSON:
{
"VLAN_MEMBER": {
"Vlan100|Ethernet24": {
"tagging_mode": "tagged"
},
"Vlan100|Ethernet28": {
"tagging_mode": "untagged"
},
}
YANG XML:
<VLAN_MEMBER>
<name>Vlan100</name>
<ifname>Ethernet24</ifname>
<tagging_mode>tagged</tagging_mode>
</VLAN_MEMBER>
<VLAN_MEMBER>
<name>Vlan100</name>
<ifname>Ethernet28</ifname>
<tagging_mode>untagged</tagging_mode>
</VLAN_MEMBER>

## Slide 15: gNMI Integration
Approach :
If path ‘Prefix’ is any of known DB name like APP_DB, CONFIG_DB etc., existing data client is created.
For other cases, new TransL data client is created.
TransL data client uses TransL Utils functions.
TransL Utils functions invoke APIs provided by TransLib library.
TransLib API creates thread internally per client subscription which listens for Redis notification. The notification data is received by TransL data client through.
Code organization:
├── dialout
│ ├── dialout_client
│ │ ├── dialout_client.go ⇒ Modified
│ │ └── dialout_client_test.go
│ ├── dialout_client_cli
│ └── dialout_client_cli.go
├── gnmi_server
│ ├── client_subscribe.go ⇒ Modified
│ ├── server.go ⇒ Modified
│ └── server_test.go
├── sonic_data_client
│ ├── db_client.go
│ ├── non_db_client.go
│ ├── transl_client.go ==> Added TransL data client
│ ├── trie.go
│ └── virtual_db.go
└── transl_utils
└── transl_utils.go ==> Added TransL Utils Layer